/* B3 (THREE PHASE TRANSFORMERS INCLUDING 44 KV & CAPACITORS

/* FIND TEMP TO FIND THE TEMPORARY END OF THIS FILE
/* THIS LINE SHOULD BE THE LAST LINE OF THE FILE TO RUN ALL CONTINGENCIES
/* TO TEST A SMALLER PORTION OF THIS FILE, MOVE THE LAST LINE WITH:  END  /* TEMP
/* TO A NEW LOCATION.  PLEASE MOVE LINE BACK TO END OF FILE WHEN DONE TESTING
/*
CONTINGENCY GETESTLOAD /*01272012 Adding load for GE Gas Turbine test motor
INCREASE BUS 307000 LOAD BY 58 MW
END
/* new way to take out autotxs rev 081310
CONTINGENCY ALLEN6
TRIP BUS 309547
END
CONTINGENCY ALLEN2  /* old way
OPEN BRANCH FROM BUS 306331 TO BUS 308502 CKT 2B
OPEN BRANCH FROM BUS 306341 TO BUS 308502 CKT Z6   /* 02032012 added z
OPEN BRANCH FROM BUS 308502 TO BUS 308750 CKT Z5   /* 02032012 added z
END
CONTINGENCY ANDERS1
TRIP BUS 309401
END
CONTINGENCY ANDERS2
TRIP BUS 309402
END
CONTINGENCY ANDERS4
TRIP BUS 309403
END
CONTINGENCY ANDERS3 /* 230-44
close BRANCH FROM BUS 309402 TO BUS 307005 CKT 2
OPEN BRANCH FROM BUS 306003 TO BUS 307005 CKT 3
END
CONTINGENCY BECKERDITE1
TRIP BUS 309505
END
CONTINGENCY BECKERDITE2
TRIP BUS 309506
END
CONTINGENCY BECKERDITE3
TRIP BUS 309507
END
CONTINGENCY BECKERDITE4
TRIP BUS 309508
END
CONTINGENCY BUCK3
TRIP BUS 309509
END
CONTINGENCY BUCK4
TRIP BUS 309510
END
CONTINGENCY BUSH1  /* DIDN'T DO close B/C ALL TERTS CLOSED
TRIP BUS 309404
END	
CONTINGENCY CENTRAL1
TRIP BUS 309405
END
CONTINGENCY CENTRAL2
TRIP BUS 309406
END
CONTINGENCY CENTRAL3
TRIP BUS 309407
END
CONTINGENCY CENTRAL4    /* jcc corrected bus # 04212011
TRIP BUS 309408
END
CONTINGENCY CENTRAL2&C /* closed
CLOSE BRANCH FROM BUS 307040 to bus 309405 ckt 1
TRIP BUS 309406
END
CONTINGENCY CENTRAL3&C /* closed
CLOSE BRANCH FROM BUS 307040 to bus 309405 ckt 1
TRIP BUS 309407
END
CONTINGENCY CENTRAL4&C /* closed   /* jcc corrected bus # 04212011
CLOSE BRANCH FROM BUS 307040 to bus 309405 ckt 1
TRIP BUS 309408
END
CONTINGENCY CLIFFSI1
TRIP BUS 309409
END
CONTINGENCY CLIFFSI2
TRIP BUS 309410
END
CONTINGENCY CLIFFSI1&C /* closed
CLOSE BRANCH FROM BUS 307431 TO BUS 309410 CKT A2
TRIP BUS 309409
END
CONTINGENCY EDURHA1
TRIP BUS 309548
END
CONTINGENCY EDURHA2
TRIP BUS 309549
END
CONTINGENCY ENO1
TRIP BUS 309411
END
CONTINGENCY ENO2
TRIP BUS 309412
END
CONTINGENCY ENO3
TRIP BUS 309413
END
CONTINGENCY ENO4
TRIP BUS 309414
END
CONTINGENCY ENO1&C /* closed
CLOSE BRANCH FROM BUS 308422 to bus 309412 ckt 2
TRIP BUS 309411
END
CONTINGENCY ENO3&C /* closed
CLOSE BRANCH FROM BUS 308422 to bus 309412 ckt 2
TRIP BUS 309413
END
CONTINGENCY ESPARBK2    /* CVA added 04112013
TRIP BRANCH FROM BUS 309372 TO BUS 307450 CKT 2
END
CONTINGENCY ESPARBK3    /* CVA added 04112013
TRIP BRANCH FROM BUS 309321 TO BUS 307450 CKT 3
END
CONTINGENCY ESPARBK4    /* CVA added 04112013
TRIP BRANCH FROM BUS 309372 TO BUS 307450 CKT 4
END
CONTINGENCY HARRISB1    /* didn't do close tert b/c single tert can handle
TRIP BUS 309431
END
CONTINGENCY HARRISB2
TRIP BUS 309415
END
CONTINGENCY HARRISB3
TRIP BUS 309416
END
CONTINGENCY HARRISB4
TRIP BUS 309417
END
CONTINGENCY HODGES1
TRIP BUS 309418
END
CONTINGENCY HODGES2
TRIP BUS 309419
END
CONTINGENCY HODGES2&C /* closed
CLOSE BRANCH FROM BUS 307088 TO BUS 309418 CKT 1
TRIP BUS 309419
END
CONTINGENCY LAKEW2 /* didn't do close tert b/c network    /* jcc corrected bus # 04212011
TRIP BUS 309420
END
CONTINGENCY LAKEW3     /* jcc corrected bus # 04212011
TRIP BUS 309421
END
CONTINGENCY LONGVIEW1  /* didn't do close tert b/c network
TRIP BUS 309422
END
CONTINGENCY LONGVIEW2
TRIP BUS 309423
END
CONTINGENCY LONGVIEW3
TRIP BUS 309424
END
CONTINGENCY LONGVIEW4      /* jcc corrected bus # 04212011
TRIP BUS 309425
END
CONTINGENCY MCDOWE1   /* 100-44
TRIP BUS 309595
END
CONTINGENCY MCDOWE1&C   /* 100-44
CLOSE BRANCH FROM BUS 307998 TO BUS 309427 CKT 2
TRIP BUS 309595
END
CONTINGENCY MCDOWE2   /* tert open
TRIP BUS 309427
END
CONTINGENCY MITCHR1
TRIP BUS 309428
END
CONTINGENCY MITCHR2
TRIP BUS 309429
END
CONTINGENCY MITCHR3
TRIP BUS 309430
END
CONTINGENCY MITCHR1&C /* closed
close BRANCH FROM BUS 308325 TO BUS 309430 CKT 3
TRIP BUS 309428
END
CONTINGENCY MITCHR2&C /* closed
close BRANCH FROM BUS 308325 TO BUS 309430 CKT 3
TRIP BUS 309429
END
CONTINGENCY MORNSTAR2
TRIP BUS 309550
END
CONTINGENCY MORNSTAR3
TRIP BUS 309551
END
CONTINGENCY MORNSTAR4
TRIP BUS 309552
END
CONTINGENCY NEWPORT1   /* didn't do close tert b/c single tert can handle
TRIP BUS 309439
END
CONTINGENCY NEWPORT2
TRIP BUS 309440
END
CONTINGENCY NEWPORT3
TRIP BUS 309441
END
CONTINGENCY NEWPORT_XFMR   /* Added to long term due to UG Bus Line with no alternate
OPEN BRANCH FROM BUS 306337 TO BUS 306333 CKT A5 
END
CONTINGENCY NGBORO1    /* DIDN'T DO B/C ALL TERTS OPEN
TRIP BUS 309432
END
CONTINGENCY NGBORO2
TRIP BUS 309433
END
CONTINGENCY NGBORO3
TRIP BUS 309434
END
CONTINGENCY NGBORO5&C /* CLOSED
CLOSE BRANCH FROM BUS 308436 TO BUS 309433 CKT 2
OPEN BRANCH FROM BUS 306943 TO BUS 308436 CKT 5
END
CONTINGENCY NGVILLE1  /* didn't do close tert b/c network    /* jcc corrected bus # 04212011
TRIP BUS 309435
END
CONTINGENCY NGVILLE2     /* jcc corrected bus # 04212011
TRIP BUS 309436
END
CONTINGENCY NGVILLE3     /* jcc corrected bus # 04212011
TRIP BUS 309437
END
CONTINGENCY NGVILLE4     /* jcc corrected bus # 04212011
TRIP BUS 309438
END
CONTINGENCY OAKBORO1 /* didn't do close tert b/c single tert can handle
TRIP BUS 309442
END
CONTINGENCY OAKBORO2
TRIP BUS 309443
END
CONTINGENCY OAKBORO3
TRIP BUS 309444
END
CONTINGENCY PACOLET1
TRIP BUS 309553
END
CONTINGENCY PACOLET2
TRIP BUS 309554
END
CONTINGENCY PACOLET3
TRIP BUS 309555
END
CONTINGENCY PARKWOOD2
TRIP BUS 309559
END
CONTINGENCY PARKWOOD3
TRIP BUS 309560
END
CONTINGENCY PEACHV1
TRIP BUS 309445
END
CONTINGENCY PEACHV2
TRIP BUS 309446
END
CONTINGENCY PEACHV3
TRIP BUS 309447
END
CONTINGENCY PEACHV3&C /* CLOSED
CLOSE BRANCH FROM BUS 307542 TO BUS 309445 CKT 1
TRIP BUS 309447
END
CONTINGENCY PEACOCK1  /* DIDN'T DO close B/C ALL TERTS CLOSED
TRIP BUS 309448
END	
CONTINGENCY PEACOCK2
TRIP BUS 309449
END
CONTINGENCY PISGAH1    /* DIDN'T DO close B/C ALL TERTS OPEN
TRIP BUS 309450
END	
CONTINGENCY PISGAH2
TRIP BUS 309451
END
CONTINGENCY PISGHBK5 /* REV. jcc 09032007
CLOSE BRANCH FROM BUS 307335 TO BUS 309450 CKT 1
CLOSE BRANCH FROM BUS 307335 TO BUS 309451 CKT 2
TRIP BRANCH FROM BUS 306190 TO BUS 307335 CKT 5
END
CONTINGENCY PLEASA1
TRIP BUS 309452
END	
CONTINGENCY PLEASA2
TRIP BUS 309453
END
CONTINGENCY PLEASA3
TRIP BUS 309454
END
CONTINGENCY PLEASA2&C /* CLOSED
CLOSE BRANCH FROM BUS 308437 TO BUS 309452 CKT 1
TRIP BUS 309453
END
CONTINGENCY ROCHESTERBK1   /* 06112013 works after 14s
CLOSE BRANCH FROM BUS 307526 TO BUS 307029 CKT 1
TRIP BRANCH FROM BUS 307525 TO BUS 307526 CKT 1
END
CONTINGENCY RURALH1 /* didn't do close tert b/c single tert can handle
TRIP BUS 309455
END	
CONTINGENCY RURALH2
TRIP BUS 309456
END
CONTINGENCY RURALH3
TRIP BUS 309457
END
CONTINGENCY SADLER3 /* didn't do close tert b/c single tert can handle
TRIP BUS 309464
END
CONTINGENCY SADLER4
TRIP BUS 309458
END
CONTINGENCY SHADYG1  /* DIDN'T DO close B/C ALL TERTS CLOSED
TRIP BUS 309459
END
CONTINGENCY SHADYG2
TRIP BUS 309460
END
CONTINGENCY SHELBY2
TRIP BUS 309461
END
CONTINGENCY SHELBY3
TRIP BUS 309462
END
CONTINGENCY SHELBY4
TRIP BUS 309463
END	
CONTINGENCY SHELBY2&C /* CLOSED
CLOSE BRANCH FROM BUS 307790 TO BUS 309462 CKT 3
TRIP BUS 309461
END
CONTINGENCY SHELBY4&C /* CLOSED
CLOSE BRANCH FROM BUS 307790 TO BUS 309462 CKT 3
TRIP BUS 309463
END	
CONTINGENCY STAMEY1
TRIP BUS 309556
END
CONTINGENCY STAMEY2
TRIP BUS 309557
END
CONTINGENCY STAMEY3
TRIP BUS 309558
END
CONTINGENCY TIGER3 /* DIDN'T DO close B/C ALL TERTS CLOSED
TRIP BUS 309465
END
CONTINGENCY TIGER5
TRIP BUS 309467
END
CONTINGENCY TIGER6   /* jcc corrected bus # 03222012
TRIP BUS 309475
END
CONTINGENCY WINECOFF1    /* jcc corrected bus # 04212011
TRIP BUS 309468
END
CONTINGENCY WINECOFF2     /* jcc corrected bus # 04212011
TRIP BUS 309469
END
CONTINGENCY WINECOFF3     /* jcc corrected bus # 04212011
TRIP BUS 309470
END
CONTINGENCY WINECOFF4     /* jcc corrected bus # 03222012
TRIP BUS 309474
END
CONTINGENCY WINECOFF1&C /* closed     /* jcc corrected bus # 04212011
close BRANCH FROM BUS 308223 TO BUS 309469 CKT 2
TRIP BUS 309468
END
CONTINGENCY WINECOFF3&C /* closed    /* jcc corrected bus # 04212011
close BRANCH FROM BUS 308223 TO BUS 309469 CKT 2
TRIP BUS 309470
END
CONTINGENCY WINECOFF4&C /* closed    /* jcc corrected bus # 03222012
close BRANCH FROM BUS 308223 TO BUS 309469 CKT 2
TRIP BUS 309474
END
CONTINGENCY WOODLA4 /* didn't do close tert b/c network
TRIP BUS 309471
END
CONTINGENCY WOODLA5
TRIP BUS 309472
END
CONTINGENCY WOODLA6
TRIP BUS 309473
END

/**************************  ZONE 1, 2, 3 BEGIN  ********************************/
CONTINGENCY BELTBK1
TRIP BRANCH FROM BUS 309301 TO BUS 307015 CKT 1
END
CONTINGENCY BELTBK2
TRIP BRANCH FROM BUS 309301 TO BUS 307015 CKT 2
END
CONTINGENCY BELTBK3
TRIP BRANCH FROM BUS 309301 TO BUS 307015 CKT 3
END
CONTINGENCY BLKGBK3
TRIP BRANCH FROM BUS 309318 TO BUS 307400 CKT 3
END
CONTINGENCY BLKGBK4
TRIP BRANCH FROM BUS 309318 TO BUS 307400 CKT 4
END
CONTINGENCY CAMPOBK2
TRIP BRANCH FROM BUS 309309 TO BUS 307246 CKT 2
END
CONTINGENCY CAMPOBK3
TRIP BRANCH FROM BUS 309309 TO BUS 307246 CKT 3
END
CONTINGENCY CAMPOBK4
TRIP BRANCH FROM BUS 309309 TO BUS 307246 CKT 4
END
CONTINGENCY CENTRLW /* in here because the central wh is a backup to oconee and can be out long term
TRIP BRANCH FROM BUS 306017 TO BUS 306041 CKT 1
END
CONTINGENCY CHESNBK2
TRIP BRANCH FROM BUS 309320 TO BUS 307425 CKT 2
END
CONTINGENCY CHESNBK3
TRIP BRANCH FROM BUS 309320 TO BUS 307425 CKT 3
END
CONTINGENCY CLARKBK1  /*   (other bank is already open in 04s case)
TRIP BRANCH FROM BUS 309302 TO BUS 307041 CKT 1
END
/* CONTINGENCY CLARKBK2
/* TRIP BRANCH FROM BUS 309302 TO BUS 307041 CKT 2 (NORMALLY OPEN REV. 3/99 MAP)
/* END
CONTINGENCY CORONBK2
TRIP BRANCH FROM BUS 306028 TO BUS 307049 CKT 2
END
CONTINGENCY CORONBK3
TRIP BRANCH FROM BUS 306028 TO BUS 307049 CKT 3
END
CONTINGENCY CORONBK4
TRIP BRANCH FROM BUS 306028 TO BUS 307049 CKT 4
END
CONTINGENCY CRETOBK4
CLOSE BRANCH FROM BUS 307036 TO BUS 307134 CKT 1
CLOSE BRANCH FROM BUS 307081 TO BUS 308807 CKT 1       /*06042013 CVA added this row                         
TRIP BRANCH FROM BUS 306029 TO BUS 307050 CKT 4
END
CONTINGENCY CYPRSBK2
TRIP BRANCH FROM BUS 306030 TO BUS 307051 CKT 2
OPEN BUS 309072 /* OPENED CAP TO STOP TOGGLING
END
CONTINGENCY CYPRSBK3
TRIP BRANCH FROM BUS 306030 TO BUS 307051 CKT 3
OPEN BUS 309072 /* OPENED CAP TO STOP TOGGLING
END
CONTINGENCY EASLYBK4
TRIP BRANCH FROM BUS 309383 TO BUS 307258 CKT 4
END
CONTINGENCY EASLYBK5
TRIP BRANCH FROM BUS 309383 TO BUS 307258 CKT 5
END
CONTINGENCY FAIRBK1
TRIP BRANCH FROM BUS 309322 TO BUS 307459 CKT 1
END
CONTINGENCY FAIRBK2
TRIP BRANCH FROM BUS 309322 TO BUS 307459 CKT 2
END
CONTINGENCY FAIRBK3
TRIP BRANCH FROM BUS 309322 TO BUS 307459 CKT 3
END
CONTINGENCY GREENVBK6
TRIP BRANCH FROM BUS 306155 TO BUS 307275 CKT 6
END
CONTINGENCY GREENVBK7
TRIP BRANCH FROM BUS 309311 TO BUS 307275 CKT 7
END
CONTINGENCY GREENVBK8
TRIP BRANCH FROM BUS 309311 TO BUS 307275 CKT 8
END
CONTINGENCY GREENWBK1
TRIP BRANCH FROM BUS 309303 TO BUS 307073 CKT 1
END
CONTINGENCY GREENWBK2
TRIP BRANCH FROM BUS 309303 TO BUS 307073 CKT 2
END
CONTINGENCY GREENWBK3
TRIP BRANCH FROM BUS 309303 TO BUS 307073 CKT 3
END
CONTINGENCY HENDBK2
TRIP BRANCH FROM BUS 309312 TO BUS 307283 CKT 2
END
CONTINGENCY HENDBK3
TRIP BRANCH FROM BUS 309312 TO BUS 307283 CKT 3
END
CONTINGENCY HORSEBK3
TRIP BRANCH FROM BUS 309371 TO BUS 307284 CKT 3
END
CONTINGENCY HORSEBK4
TRIP BRANCH FROM BUS 309371 TO BUS 307284 CKT 4
END
CONTINGENCY INMANBK1
TRIP BRANCH FROM BUS 309323 TO BUS 307479 CKT 1
END
CONTINGENCY INMANBK2
TRIP BRANCH FROM BUS 309323 TO BUS 307479 CKT 2
END
CONTINGENCY INMANK3
TRIP BRANCH FROM BUS 309323 TO BUS 307479 CKT 3
END
CONTINGENCY LAWSNBK1
TRIP BRANCH FROM BUS 306269 TO BUS 307504 CKT 1
OPEN BUS 309096 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY LAWSNBK2
TRIP BRANCH FROM BUS 306269 TO BUS 307504 CKT 3 /* if skipped, you can open cap (see line below)
/* OPEN BUS 309096 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY LIONMTNBK2
TRIP BRANCH FROM BUS 309308 TO BUS 307211 CKT 2
END
CONTINGENCY LIONMTNBK3
TRIP BRANCH FROM BUS 309308 TO BUS 307211 CKT 3
END
CONTINGENCY MARIEBK2
TRIP BRANCH FROM BUS 309314 TO BUS 307309 CKT 2
END
CONTINGENCY MARIEBK3
TRIP BRANCH FROM BUS 309314 TO BUS 307309 CKT 3
END
CONTINGENCY PICKBK1      /* 02242012 CVA revised bus #
TRIP BRANCH FROM BUS 306188 TO BUS 307333 CKT 1
END
CONTINGENCY PICKBK2      /* 02242012 CVA revised bus #
TRIP BRANCH FROM BUS 306188 TO BUS 307333 CKT 2
END
CONTINGENCY PICKBK3      /* 02242012 CVA revised bus #
TRIP BRANCH FROM BUS 306188 TO BUS 307333 CKT 3
END
CONTINGENCY PINKBK2
TRIP BRANCH FROM BUS 309326 TO BUS 307548 CKT 2
END
CONTINGENCY PINKBK3
TRIP BRANCH FROM BUS 309326 TO BUS 307548 CKT 3
END
CONTINGENCY SANDYBK1
TRIP BRANCH FROM BUS 309304 TO BUS 307149 CKT 1
END
CONTINGENCY SANDYBK2
TRIP BRANCH FROM BUS 309304 TO BUS 307149 CKT 2
END
CONTINGENCY SENECA1
TRIP BRANCH FROM BUS 309305 TO BUS 307154 CKT 1
END
CONTINGENCY SENECA2
TRIP BRANCH FROM BUS 309305 TO BUS 307154 CKT 2
END
CONTINGENCY TOXAWYBK1
TRIP BRANCH FROM BUS 306066 TO BUS 307167 CKT 1
END
CONTINGENCY TOXAWYBK2
TRIP BRANCH FROM BUS 306066 TO BUS 307167 CKT 2
END
CONTINGENCY WALHABK2
TRIP BRANCH FROM BUS 309306 TO BUS 307177 CKT 2
END
CONTINGENCY WALHABK3
TRIP BRANCH FROM BUS 309306 TO BUS 307177 CKT 3
END
CONTINGENCY WALHABK4
TRIP BRANCH FROM BUS 309306 TO BUS 307177 CKT 4
END
CONTINGENCY WESTMINBK1
TRIP BRANCH FROM BUS 309307 TO BUS 307190 CKT 1
END
CONTINGENCY WESTMINBK2
TRIP BRANCH FROM BUS 309307 TO BUS 307190 CKT 2
END
CONTINGENCY WESTMINBK3
TRIP BRANCH FROM BUS 309307 TO BUS 307190 CKT 3
END
CONTINGENCY WSPRTBK2
TRIP BRANCH FROM BUS 309327 TO BUS 307604 CKT 2
/*OPEN BUS 309099 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY WSPRTBK3
TRIP BRANCH FROM BUS 309327 TO BUS 307604 CKT 3
/*OPEN BUS 309099 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY WOODRBK1
TRIP BRANCH FROM BUS 309328 TO BUS 307608 CKT 1
/*OPEN BUS 309100 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY WOODRBK2
TRIP BRANCH FROM BUS 309328 TO BUS 307608 CKT 2
/*OPEN BUS 309100 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY WOODRBK3
TRIP BRANCH FROM BUS 309328 TO BUS 307608 CKT 3
/*OPEN BUS 309100 /* OPENED CAP TO STOP TOGGLING PWM 3-01
END
CONTINGENCY THORPEBK2
OPEN BRANCH FROM BUS 308486 TO BUS 308515 CKT 2
END
CONTINGENCY TUCKASEEBK2
OPEN BRANCH FROM BUS 308489 TO BUS 308487 CKT 2
END
CONTINGENCY TUCKASEEBK3
OPEN BRANCH FROM BUS 308489 TO BUS 308487 CKT 3
END
CONTINGENCY WEBSTERBK1
OPEN BRANCH FROM BUS 308488 TO BUS 308555 CKT 1
END
CONTINGENCY WESTMILLBK2         /* THIS BANK IS GOING AWAY
OPEN BRANCH FROM BUS 308484 TO BUS 308590 CKT 2
END
CONTINGENCY LAKEEMORYBK1
OPEN BRANCH FROM BUS 308482 TO BUS 308595 CKT 1
END
CONTINGENCY SWAINBK1&BK2
OPEN BRANCH FROM BUS 308571 TO BUS 308581 CKT Z1
END
CONTINGENCY SWAINBK3
OPEN BRANCH FROM BUS 308571 TO BUS 308591 CKT Z1
END
/**************************   ZONE 1, 2, 3 END   ********************************/
/**************************   ZONE 4, 5 BEGIN   *********************************/

CONTINGENCY DIXIE2
OPEN BRANCH FROM BUS 309334 TO BUS 307669 CKT 2
END
CONTINGENCY DIXIE3
OPEN BRANCH FROM BUS 309334 TO BUS 307669 CKT 3
END
CONTINGENCY TABLEROCK1
OPEN BRANCH FROM BUS 309349 TO BUS 308055 CKT 1
END
CONTINGENCY TABLEROCK2
OPEN BRANCH FROM BUS 309349 TO BUS 308055 CKT 2
END
CONTINGENCY TABLEROCK3
OPEN BRANCH FROM BUS 309349 TO BUS 308055 CKT 3
END
CONTINGENCY ACREROCK2
OPEN BRANCH FROM BUS 309329 TO BUS 307631 CKT 2
END
CONTINGENCY ACREROCK3
OPEN BRANCH FROM BUS 309329 TO BUS 307631 CKT 3
END
CONTINGENCY BELMONT2
OPEN BRANCH FROM BUS 309330 TO BUS 307639 CKT 2
END
CONTINGENCY BELMONT3
OPEN BRANCH FROM BUS 309330 TO BUS 307639 CKT 3
END
CONTINGENCY CHERRYV2
OPEN BRANCH FROM BUS 309332 TO BUS 307658 CKT 2
END
CONTINGENCY CHERRYV3
OPEN BRANCH FROM BUS 309332 TO BUS 307658 CKT 3
END
CONTINGENCY CHERRYV4
OPEN BRANCH FROM BUS 309332 TO BUS 307658 CKT 4
END
CONTINGENCY CLOVER1
OPEN BRANCH FROM BUS 309333 TO BUS 307663 CKT 1
END
CONTINGENCY CLOVER2
OPEN BRANCH FROM BUS 309333 TO BUS 307663 CKT 2
END
CONTINGENCY GREATF1
OPEN BRANCH FROM BUS 309336 TO BUS 307701 CKT 1
END
CONTINGENCY GREATF2
OPEN BRANCH FROM BUS 309336 TO BUS 307701 CKT 2
END
CONTINGENCY HICKORY1
OPEN BRANCH FROM BUS 309341 TO BUS 307975 CKT 1
END
CONTINGENCY HICKORY2
OPEN BRANCH FROM BUS 309341 TO BUS 307975 CKT 2
END
CONTINGENCY HICKORY3
OPEN BRANCH FROM BUS 306465 TO BUS 307975 CKT 3
END
CONTINGENCY HILLTOP1
OPEN BRANCH FROM BUS 309337 TO BUS 307709 CKT 1
END
CONTINGENCY HILLTOP2
OPEN BRANCH FROM BUS 309337 TO BUS 307709 CKT 2
END
CONTINGENCY HILLTOP3
OPEN BRANCH FROM BUS 309373 TO BUS 307709 CKT 3
END
CONTINGENCY HILLTOP4
OPEN BRANCH FROM BUS 309373 TO BUS 307709 CKT 4
END
CONTINGENCY LINCOLNTON5
OPEN BRANCH FROM BUS 309342 TO BUS 307986 CKT 5
END
CONTINGENCY LINCOLNTON6
OPEN BRANCH FROM BUS 309342 TO BUS 307986 CKT 6
END
CONTINGENCY LOOKOUT1
OPEN BRANCH FROM BUS 309343 TO BUS 307992 CKT 1
END
CONTINGENCY LOOKOUT2
OPEN BRANCH FROM BUS 309343 TO BUS 307992 CKT 2
END
CONTINGENCY LOOKOUT3
OPEN BRANCH FROM BUS 309343 TO BUS 307992 CKT 3
END
CONTINGENCY MCADENV2
OPEN BRANCH FROM BUS 309339 TO BUS 307744 CKT 2
END
CONTINGENCY MCADENV3
OPEN BRANCH FROM BUS 309339 TO BUS 307744 CKT 3
END
CONTINGENCY MCADENV4
OPEN BRANCH FROM BUS 309339 TO BUS 307744 CKT 4
END
CONTINGENCY MILLRH1
OPEN BRANCH FROM BUS 306474 TO BUS 308000 CKT 1
END
CONTINGENCY MILLRH2
OPEN BRANCH FROM BUS 306474 TO BUS 308000 CKT 2
END
CONTINGENCY MILLRH3
OPEN BRANCH FROM BUS 306474 TO BUS 308000 CKT 3
END
CONTINGENCY MILLRH4
OPEN BRANCH FROM BUS 306474 TO BUS 308000 CKT 4
END
CONTINGENCY MORGANTON5
OPEN BRANCH FROM BUS 309344 TO BUS 308005 CKT 5
END
CONTINGENCY MORGANTON6
OPEN BRANCH FROM BUS 309344 TO BUS 308005 CKT 6
END
CONTINGENCY MORGANTON7
OPEN BRANCH FROM BUS 309344 TO BUS 308005 CKT 7
END
CONTINGENCY RHODHISS5
OPEN BRANCH FROM BUS 309346 TO BUS 308028 CKT 5
END
CONTINGENCY RHODHISS6
OPEN BRANCH FROM BUS 309346 TO BUS 308028 CKT 6
END
CONTINGENCY TAYLORSV1
OPEN BRANCH FROM BUS 309350 TO BUS 308066 CKT 1
END
CONTINGENCY TAYLORSV2
OPEN BRANCH FROM BUS 309350 TO BUS 308066 CKT 2
END
CONTINGENCY VANWYCK1
OPEN BRANCH FROM BUS 306415 TO BUS 307829 CKT 1
END
CONTINGENCY VANWYCK2
OPEN BRANCH FROM BUS 306415 TO BUS 307829 CKT 2
END
CONTINGENCY WYLIE5
OPEN BRANCH FROM BUS 309340 TO BUS 307839 CKT 5
END
CONTINGENCY WYLIE6
OPEN BRANCH FROM BUS 309340 TO BUS 307839 CKT 6
END
CONTINGENCY WALKERBK3
OPEN BRANCH FROM BUS 309331 TO BUS 307842 CKT 3
END
CONTINGENCY WALKERBK2
OPEN BRANCH FROM BUS 309331 TO BUS 307842 CKT 2
END
CONTINGENCY SUGARHILL2
OPEN BRANCH FROM BUS 309348 TO BUS 308052 CKT 2
END
CONTINGENCY SUGARHILL3
OPEN BRANCH FROM BUS 309348 TO BUS 308052 CKT 3
END
/***************************   ZONE 4, 5 END   **********************************/
/***************************   ZONE 6 BEGIN   ***********************************/
CONTINGENCY STATES1
OPEN BRANCH FROM BUS 309347 TO BUS 308051 CKT 1
END
CONTINGENCY STATES3
OPEN BRANCH FROM BUS 309347 TO BUS 308051 CKT 3
END
CONTINGENCY STATES2
OPEN BRANCH FROM BUS 309347 TO BUS 308051 CKT 2
END
CONTINGENCY CHINAGR2
OPEN BRANCH FROM BUS 309352 TO BUS 308124 CKT 2
END
CONTINGENCY CHINAGR3
OPEN BRANCH FROM BUS 309352 TO BUS 308124 CKT 3
END
CONTINGENCY CHINAGR4
OPEN BRANCH FROM BUS 309352 TO BUS 308124 CKT 4
END
CONTINGENCY CONCORD7
OPEN BRANCH FROM BUS 309374 TO BUS 308132 CKT 7
END
CONTINGENCY CONCORD8
OPEN BRANCH FROM BUS 309374 TO BUS 308132 CKT 8
END
CONTINGENCY CONCORDCY2
OPEN BRANCH FROM BUS 309353 TO BUS 308234 CKT 2
END
CONTINGENCY CONCORDCY1
OPEN BRANCH FROM BUS 309353 TO BUS 308234 CKT 1
END
CONTINGENCY MOCKS4
OPEN BRANCH FROM BUS 309354 TO BUS 308173 CKT 4
END
CONTINGENCY MOCKS5
OPEN BRANCH FROM BUS 309354 TO BUS 308173 CKT 5
END
CONTINGENCY MOCKS6
OPEN BRANCH FROM BUS 309354 TO BUS 308173 CKT 6
END
CONTINGENCY MONROEMN8
OPEN BRANCH FROM BUS 309355 TO BUS 308174 CKT 8
END
CONTINGENCY MONROEMN7
OPEN BRANCH FROM BUS 309355 TO BUS 308174 CKT 7
END
CONTINGENCY MOORES1
OPEN BRANCH FROM BUS 309356 TO BUS 308176 CKT 1
END
CONTINGENCY MOORES2
OPEN BRANCH FROM BUS 309356 TO BUS 308176 CKT 2
END
CONTINGENCY MOORES3
OPEN BRANCH FROM BUS 309375 TO BUS 308176 CKT 3
END
CONTINGENCY MOORES4
OPEN BRANCH FROM BUS 309375 TO BUS 308176 CKT 4
END
CONTINGENCY RIVERBEND1
OPEN BRANCH FROM BUS 306652 TO BUS 308191 CKT 1
END
CONTINGENCY RIVERBEND2
OPEN BRANCH FROM BUS 306652 TO BUS 308191 CKT 2
END
CONTINGENCY RIVERBEND3
OPEN BRANCH FROM BUS 306652 TO BUS 308191 CKT 3
END
CONTINGENCY ROUGHEDGE1A
OPEN BRANCH FROM BUS 309357 TO BUS 308194 CKT 1A
END
CONTINGENCY ROUGHEDGE1B
OPEN BRANCH FROM BUS 309357 TO BUS 308194 CKT 1B
END
CONTINGENCY WILDCAT1
OPEN BRANCH FROM BUS 309359 TO BUS 308221 CKT 1
END
CONTINGENCY WILDCAT2
OPEN BRANCH FROM BUS 309359 TO BUS 308221 CKT 2
END
CONTINGENCY WILDCAT3
OPEN BRANCH FROM BUS 309359 TO BUS 308221 CKT 3
END
/****************************   ZONE 6 END   ************************************/
/**************************  ZONE 7, 8, 9 BEGIN  ********************************/
CONTINGENCY LEXCITY1BK2
OPEN BRANCH FROM BUS 309367 TO BUS 308309 CKT 2
END
CONTINGENCY LEXCITY1BK3
OPEN BRANCH FROM BUS 309367 TO BUS 308309 CKT 3
END
CONTINGENCY ABBOTTSCK1
OPEN BRANCH FROM BUS 309366 TO BUS 308411 CKT 1
END
CONTINGENCY ABBOTTSCK2
OPEN BRANCH FROM BUS 309366 TO BUS 308411 CKT 2
END
CONTINGENCY ABBOTTSCK3
OPEN BRANCH FROM BUS 309366 TO BUS 308411 CKT 3
END
CONTINGENCY WALNUTCO1
OPEN BRANCH FROM BUS 306809 TO BUS 308371 CKT 1
END
CONTINGENCY WALNUTCO2
OPEN BRANCH FROM BUS 306809 TO BUS 308371 CKT 2
END
CONTINGENCY WILKES3
OPEN BRANCH FROM BUS 309365 TO BUS 308374 CKT 3
END
CONTINGENCY WILKES4
OPEN BRANCH FROM BUS 309365 TO BUS 308374 CKT 4
END
CONTINGENCY RUTLEDGE1
OPEN BRANCH FROM BUS 309364 TO BUS 308348 CKT 1
END
CONTINGENCY RUTLEDGE2
OPEN BRANCH FROM BUS 309364 TO BUS 308348 CKT 2
END
contingency MADISON1
OPEN BRANCH FROM BUS 309361 TO BUS 308312 CKT 1
END
contingency MADISON2
OPEN BRANCH FROM BUS 309361 TO BUS 308312 CKT 2
END
contingency MADISON3
OPEN BRANCH FROM BUS 309361 TO BUS 308312 CKT 3
END
CONTINGENCY MEBANE1
OPEN BRANCH FROM BUS 309368 TO BUS 308433 CKT 1
END
CONTINGENCY MEBANE2
OPEN BRANCH FROM BUS 309368 TO BUS 308433 CKT 2
END
CONTINGENCY MEBANE3
OPEN BRANCH FROM BUS 309368 TO BUS 308433 CKT 3
END
CONTINGENCY MEBANE4
OPEN BRANCH FROM BUS 309368 TO BUS 308433 CKT 4
END
CONTINGENCY MOTLEY1
OPEN BRANCH FROM BUS 309362 TO BUS 308328 CKT 1
END
CONTINGENCY MOTLEY2
OPEN BRANCH FROM BUS 309362 TO BUS 308328 CKT 2
END
CONTINGENCY MOTLEY3
OPEN BRANCH FROM BUS 309362 TO BUS 308328 CKT 3
END

/*CONTINGENCY NGBORO5 (power bank serving 44 kV)
/*OPEN BRANCH FROM BUS 306943 TO BUS 308436 CKT 5
/*END
CONTINGENCY SWEPSONVILL2
OPEN BRANCH FROM BUS 309369 TO BUS 308448 CKT 2
END
CONTINGENCY SWEPSONVILL3
OPEN BRANCH FROM BUS 309369 TO BUS 308448 CKT 3
END

/**************************   ZONE 7, 8, 9 END   ********************************/
/*******************   CAPACITORS AND REACTORS BEGIN   **************************/
CONTINGENCY CONCD100_CAP
OPEN BRANCH FROM BUS 306573 TO BUS 309040 CKT Z1
/* CONCORD 100 KV CAP CONTINGENCY
END
CONTINGENCY ASBURY_RCTR    /* added reactor contingencies 1/00 JCC & PWM
OPEN BUS 309003
END
CONTINGENCY KATOMA_RCTR    /* separated two oconee reactors 12/01 jcc
OPEN BUS 309011
END
CONTINGENCY RICHMOND_RCTR
OPEN BUS 309163
END
CONTINGENCY S_MOUNTAIN_RCTR
OPEN BUS 309161
END
CONTINGENCY ROCK_SPRINGS_RCTR
OPEN BUS 309162
END
CONTINGENCY GODBEY_RCTR
OPEN BUS 309164
END
CONTINGENCY HIKRY100_CAP
OPEN BUS 309030
END
CONTINGENCY CONCRD44_CAP
OPEN BUS 309129
END
CONTINGENCY TUKSG161_CAP
OPEN BUS 309154
END
CONTINGENCY NANT161_CAP
OPEN BUS 309153
END
CONTINGENCY RIVBD100_CAP
OPEN BUS 309046
END
CONTINGENCY MEBANE100CAP
OPEN BUS 309064
END
CONTINGENCY STAMEY100CAP
OPEN BUS 309034
END
CONTINGENCY BUCK100CAP
OPEN BUS 309038
END
CONTINGENCY OAKBOR100CAP
OPEN BUS 309045
END
CONTINGENCY SHAT100_CAP
OPEN BUS 309055
END
CONTINGENCY LEE100_CAP
OPEN BUS 309007
END
CONTINGENCY AMITY100_CAP
OPEN BUS 309037
END
CONTINGENCY MON10056_CAP
OPEN BUS 309042
END
CONTINGENCY MON10078_CAP
OPEN BUS 308896
END
CONTINGENCY EGRNV100_CAP
OPEN BUS 309013
END
CONTINGENCY BCKRDT10_CAP
OPEN BUS 309050
END
CONTINGENCY TIGER100_CAP
OPEN BUS 309018
END
CONTINGENCY MITCHLR_CAP
OPEN BUS 309051
END
CONTINGENCY RURALHL_CAP
OPEN BUS 309053
END
CONTINGENCY NGREENS_CAP
OPEN BUS 309067
END
CONTINGENCY BUSHRVR1_CAP
OPEN BUS 309019
END
CONTINGENCY ALBEMAR1_CAP
OPEN BUS 309036
END
CONTINGENCY WINSTON1_CAP   /* 03212013 - TRYING TO OUTAGE 2 INSTEAD OF 4
ADD SHUNT 1 TO BUS 306814
OPEN BUS 309056
END
CONTINGENCY DACIA100_CAP   /* 03212013 - TRYING TO OUTAGE 2 INSTEAD OF 4
ADD SHUNT 1 TO BUS 306941
OPEN BUS 309066
END
CONTINGENCY GLENRVN1_CAP    /* 03212013 - TRYING TO OUTAGE 2 INSTEAD OF 4
ADD SHUNT 1 TO BUS 306897
OPEN BUS 309061
END
CONTINGENCY GREENSBR_CAP
OPEN BUS 309062
END
CONTINGENCY LINDENST_CAP
OPEN BUS 309063
END
CONTINGENCY HODGS100_CAP
OPEN BUS 309006
END
CONTINGENCY NWILK100_CAP
OPEN BUS 309052
END
CONTINGENCY ANDER100_CAP
OPEN BUS 309004
END
CONTINGENCY PISGH100_CAP
OPEN BUS 309015
END
CONTINGENCY MORNSTAR_CAP
OPEN BUS 309044
END
CONTINGENCY CRETO100_CAP
OPEN BUS 309005
END
CONTINGENCY FAIRVIEW_CAP
OPEN BUS 309021
END
CONTINGENCY CHEST100_CAP
OPEN BUS 309024
END
CONTINGENCY BREED100_CAP
OPEN BUS 309029
END
CONTINGENCY SADLR100_CAP
OPEN BUS 309054
END
CONTINGENCY LOOK100_CAP
OPEN BUS 309033
END
CONTINGENCY MOCKS100_CAP
OPEN BUS 309041
END
CONTINGENCY MRSVL100_CAP
OPEN BUS 309043
END
CONTINGENCY NEWT44_CAP13
OPEN BUS 309122
END
CONTINGENCY NEWT44_CAP24
OPEN BUS 309148
END
CONTINGENCY GAFNEY44_CAP
OPEN BUS 309092
END
CONTINGENCY SANDYSP1_CAP
OPEN BUS 309008
END
CONTINGENCY REEDY100_CAP
OPEN BUS 309016
END
CONTINGENCY HILLTP44_CAP
OPEN BUS 309107
END
CONTINGENCY MADISN44_CAP
OPEN BUS 309140
END
CONTINGENCY CHRYVL44_CAP
OPEN BUS 309103
END
CONTINGENCY CONCRD44_CAP
OPEN BUS 309130
END
CONTINGENCY RHODHS44_CAP
OPEN BUS 309123
END
CONTINGENCY MCADNV44_CAP
OPEN BUS 309112
END
CONTINGENCY MILRHL44_CAP
OPEN BUS 309120
END
CONTINGENCY ENGRU32_CAP
OPEN BUS 309058
END
CONTINGENCY CAMPOB44_CAP
OPEN BUS 309081
END
CONTINGENCY INMAN44_CAP
OPEN BUS 309093
END
CONTINGENCY LARENS44_CAP
OPEN BUS 309095
END
CONTINGENCY ABOTSC44_CAP
OPEN BUS 309150
END
CONTINGENCY CORONA44_CAP
OPEN BUS 309071
END
CONTINGENCY WODRUF44_CAP
OPEN BUS 309100
END
CONTINGENCY HICKRY44_CAP
OPEN BUS 309117
END
CONTINGENCY MRGNTN44_CAP
OPEN BUS 309121
END
CONTINGENCY FAIRVW44_CAP
OPEN BUS 309091
END
CONTINGENCY CYPRES44_CAP
OPEN BUS 309072
END
CONTINGENCY HNDRSV44_CAP
OPEN BUS 309083
END
CONTINGENCY ACRERK44_CAP
OPEN BUS 309101
END
CONTINGENCY MEBANE44_CAP
OPEN BUS 309151
END
CONTINGENCY LINCLNT4_CAP
OPEN BUS 309118
END
CONTINGENCY ANDRSN44_CAP
OPEN BUS 309070
END
CONTINGENCY SPARTB44_CAP
OPEN BUS 309099
END
CONTINGENCY SUGRHL44_CAP
OPEN BUS 309125
END
CONTINGENCY NINET944_CAP
OPEN BUS 309113
END
CONTINGENCY WALHAL44_CAP
OPEN BUS 309078
END
CONTINGENCY WALNTC44_CAP
OPEN BUS 309146
END
CONTINGENCY WILKST44_CAP
OPEN BUS 309147
END
CONTINGENCY BELWOD44_CAP
OPEN BUS 309102
END
CONTINGENCY SENECA44_CAP
OPEN BUS 309076
END
CONTINGENCY LOOKOT44_CAP
OPEN BUS 309119
END
CONTINGENCY MOCKVL44_CAP
OPEN BUS 309131
END
CONTINGENCY CLINTN44_CAP
OPEN BUS 309090
END
CONTINGENCY WESTMN44_CAP
OPEN BUS 309079
END
CONTINGENCY MARIET44_CAP
OPEN BUS 309085
END
CONTINGENCY TURNER44_CAP
OPEN BUS 309098
END
CONTINGENCY CLOVER44_CAP
OPEN BUS 309104
END
CONTINGENCY CNCRD_C_CAP
OPEN BUS 309138
END
CONTINGENCY MOTLEY44_CAP
OPEN BUS 309141
END
CONTINGENCY RUTLDG44_CAP
OPEN BUS 309144
END
CONTINGENCY AMTHRE44_CAP
OPEN BUS 309116
END
CONTINGENCY HNSLYR44_CAP
OPEN BUS 309108
END
CONTINGENCY JOANNA44_CAP
OPEN BUS 309075
END
CONTINGENCY PICKNS44_CAP
OPEN BUS 309086
END
CONTINGENCY TYLRSVL_CAP
OPEN BUS 309127
END
CONTINGENCY PINACL44_CAP
OPEN BUS 309142
END
CONTINGENCY SWEPSV44_CAP
OPEN BUS 309152
END
CONTINGENCY PRSTNVL_CAP
OPEN BUS 309143
END
CONTINGENCY CANECK100_CAP
OPEN BUS 309012
END
CONTINGENCY CANECK44_CAP
OPEN BUS 309082
END
CONTINGENCY REEDYR4_CAP
OPEN BUS 309088
END
CONTINGENCY TABLRK44_CAP
OPEN BUS 309126
END
CONTINGENCY MORESVIL_CAP
OPEN BUS 309133
END
CONTINGENCY CHESNEE4_CAP
OPEN BUS 309089
END
CONTINGENCY LANCAST4_CAP
OPEN BUS 309111
END
CONTINGENCY ROUGHED4_CAP
OPEN BUS 309136
END
CONTINGENCY GTFALL44_CAP
OPEN BUS 309106
END
CONTINGENCY LAWSONF4_CAP
OPEN BUS 309096
END
CONTINGENCY MONROE44_CAP
OPEN BUS 309132
END
CONTINGENCY TOXAWY44_CAP
OPEN BUS 309077
END
CONTINGENCY FORESTLK_CAP
OPEN BUS 309134
END
/*CONTINGENCY GASTNJ44_CAP
/*OPEN BUS 6690
/*END
CONTINGENCY FLDCN19_CAP
OPEN BUS 309105
END
CONTINGENCY KERSHAW_CAP
OPEN BUS 309109
END
CONTINGENCY BOWWTR10_CAP
OPEN BUS 309026
END
CONTINGENCY ESPAR100_CAP
OPEN BUS 309020
END
CONTINGENCY WSPAR100_CAP
OPEN BUS 309023
END
CONTINGENCY RVRBND44_CAP
OPEN BUS 309135
END
CONTINGENCY VALDSE44_CAP
OPEN BUS 309128
END
CONTINGENCY 1WYLIE44_CAP
OPEN BUS 309115
END
CONTINGENCY STATSVL4_CAP
OPEN BUS 309124
END
CONTINGENCY WLDCAT44_CAP
OPEN BUS 309137
END
CONTINGENCY CHINA100_CAP
OPEN BUS 309039
END
CONTINGENCY PLEAS100_CAP
OPEN BUS 309069
END
CONTINGENCY ENO100_CAP
OPEN BUS 309060
END
CONTINGENCY PARKW100_CAP   /* 03212013 - TRYING TO OUTAGE 2 INSTEAD OF 4
ADD SHUNT 1 TO BUS 306948
OPEN BUS 309068
END
CONTINGENCY WINE100_CAP
OPEN BUS 309047
END
CONTINGENCY GRENL100_CAP
OPEN BUS 309014
END
CONTINGENCY HORSE44_CAP
OPEN BUS 309084
END
CONTINGENCY KINGSM44_CAP
OPEN BUS 309110
END
CONTINGENCY LONGV100_CAP
OPEN BUS 309032
END
CONTINGENCY LANC100_CAP
OPEN BUS 309027
END
CONTINGENCY LINC100_CAP
OPEN BUS 309031
END
CONTINGENCY WESTSMILLCAP   /* WILL BE REMOVED BEYOND 12
OPEN BUS 309158
END
CONTINGENCY SHADY100_CAP
OPEN BUS 309017
END
CONTINGENCY SURRY4_44CAP
OPEN BUS 309145
END
CONTINGENCY WOODL100_CAP
OPEN BUS 309048
END
CONTINGENCY WYLIE100_CAP
OPEN BUS 309028
END
CONTINGENCY BANRTOWN_CAP
OPEN BUS 309049
END
CONTINGENCY WEBSTER_CAP
OPEN BUS 309156
END
CONTINGENCY L_EMORY66CAP
OPEN BUS 309159
END
CONTINGENCY THORPE66CAP
OPEN BUS 309155
END
CONTINGENCY HYATT66CAP
OPEN BUS 309157
END
CONTINGENCY BREC1644_CAP
OPEN BUS 309080
END
CONTINGENCY LAU744_CAP
OPEN BUS 309094
END
CONTINGENCY RUEMC544_CAP
OPEN BUS 309114
END
CONTINGENCY RUEMC744_CAP
OPEN BUS 309097
END
CONTINGENCY PISGH44_CAP
OPEN BUS 309087
END
CONTINGENCY BLWSCK230CAP
OPEN BUS 308898
END
/********************   CAPACITORS AND REACTORS END   ***************************/
/*****************************   BULK BEGIN   ***********************************/
CONTINGENCY COWANSW_GSU
OPEN BUS 308541
MOVE 100 percent GENERATION FROM BUS 308227 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 308237 TO BUS 1
END
CONTINGENCY ROCK_BL1GSU
/* OPEN BRANCH FROM BUS 308500 TO BUS 306826 CKT Z1 /* 6ROCKHMBKL1 230 - 6ERNEST2 230 */
OPEN BRANCH FROM BUS 306828 TO BUS 308500 CKT 4 /* 6ROCKHMBKL1 230 - 1ROCKHMG04 , 02032012 chg fr 306500 to 308500 */
OPEN BRANCH FROM BUS 306829 TO BUS 308500 CKT 5 /* 6ROCKHMBKL1 230 - 1ROCKHMG05 , 02032012 chg fr 306500 to 308500 */
MOVE 100 percent GENERATION FROM BUS 306828 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306829 TO BUS 1
END
CONTINGENCY ROCK_BL2GSU
/* OPEN BRANCH FROM BUS 308501 TO BUS 306827 CKT Z2 /* 6ROCKHMBKL2 230 - 6ERNEST1 230 */
OPEN BRANCH FROM BUS 306831 TO BUS 308501 CKT 1 /* 6ROCKHMBKL2 230 - 1ROCKHMG01 , 02032012 chg fr 306501 to 308501 */
OPEN BRANCH FROM BUS 306832 TO BUS 308501 CKT 2 /* 6ROCKHMBKL2 230 - 1ROCKHMG02 , 02032012 chg fr 306501 to 308501 */
OPEN BRANCH FROM BUS 306833 TO BUS 308501 CKT 3 /* 6ROCKHMBKL2 230 - 1ROCKHMG03 , 02032012 chg fr 306501 to 308501 */
MOVE 100 percent GENERATION FROM BUS 306831 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306832 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306833 TO BUS 1
END
CONTINGENCY MLCK_BL1GSU1
OPEN BUS 308396
MOVE 100 percent GENERATION FROM BUS 306082 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306083 TO BUS 1
END
CONTINGENCY MLCK_BL1GSU2
OPEN BUS 308397
MOVE 100 percent GENERATION FROM BUS 306084 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306086 TO BUS 1
END
CONTINGENCY MLCK_BL2GSU1
OPEN BUS 308398
MOVE 100 percent GENERATION FROM BUS 306087 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306088 TO BUS 1
END
CONTINGENCY MLCK_BL2GSU2
OPEN BUS 308399
MOVE 100 percent GENERATION FROM BUS 306090 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306091 TO BUS 1
END
CONTINGENCY CHEROKEE_GSU
OPEN BRANCH FROM BUS 306324 TO BUS 306325 CKT 1
OPEN BRANCH FROM BUS 306324 TO BUS 306326 CKT 1
MOVE 100 percent GENERATION FROM BUS 306325 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 306326 TO BUS 1
END
CONTINGENCY KEOWEE_GSU
OPEN BUS 308544
MOVE 100 percent GENERATION FROM BUS 307195 TO BUS 1
MOVE 100 percent GENERATION FROM BUS 308880 TO BUS 1
END
CONTINGENCY JOCASSE_XFMR
OPEN BRANCH FROM BUS 306113 TO BUS 307690 CKT 1 /* 8JOCASSE 500 - 6JOCASSE 230 , 02032012 chg fr 306106 to 307690 */
END
CONTINGENCY BUSHR1151006
OPEN BRANCH FROM BUS 306231 TO BUS 306242 CKT 6 /* 3BUSH Y  115 - BUSH RIV 100 */
END
CONTINGENCY BUSHYEL7_8
OPEN BRANCH FROM BUS 306232 TO BUS 309319 CKT 7 /* 3BUSH R  115 - BUSH RI2 100 */
OPEN BRANCH FROM BUS 306232 TO BUS 309319 CKT 8 /* 3BUSH R  115 - BUSH RI2 100 */
END
CONTINGENCY CLARK115100
OPEN BRANCH FROM BUS 306001 TO BUS 306022 CKT 4 /* 3CLARK H 115 - CLARK HL 100 */
END
CONTINGENCY HORSE1151&2
OPEN BRANCH FROM BUS 306101 TO BUS 309313 CKT 1 /* 3HORSESH 115 - HORSESH2 100 */
OPEN BRANCH FROM BUS 306101 TO BUS 309313 CKT 2 /* 3HORSESH 115 - HORSESH2 100 */
END
CONTINGENCY HORSE1151001
OPEN BRANCH FROM BUS 306101 TO BUS 309313 CKT 1 /* 3HORSESH 115 - HORSESH2 100 */
END
CONTINGENCY HORSE1151002
OPEN BRANCH FROM BUS 306101 TO BUS 309313 CKT 2 /* 3HORSESH 115 - HORSESH2 100 */
END
/* CONTINGENCY WATERE100115
/* OPEN BRANCH FROM BUS    306416 TO BUS  40734 CKT 1  /* WATEREE  100 - 3WATRE   115 */
/* END
CONTINGENCY WATERE100115
OPEN BRANCH FROM BUS 306416 TO BUS 304734 CKT 1 /* WATEREE  100 - WATRE    115 */
END
CONTINGENCY DANRV1001381
OPEN BRANCH FROM BUS 309360 TO BUS 306711 CKT 1 /* DANRVR   100 - 4DAN RIV 138 */
END
CONTINGENCY DANRV1001382
OPEN BRANCH FROM BUS 309360 TO BUS 306711 CKT 2 /* DANRVR   100 - 4DAN RIV 138 */
END
/* CONTINGENCY BADIN1001151
/* TRIP BRANCH FROM BUS   339001 TO BUS  40342 CKT 1  /* BADIN    100 - 3BADIN 1 115 */
/* END
CONTINGENCY BADIN1001151
TRIP BRANCH FROM BUS 339001 TO BUS 304342 CKT 1 /* BADIN    100 - BADIN #1 115 */
END
/* CONTINGENCY BADIN1001152
/* TRIP BRANCH FROM BUS   339001 TO BUS  40343 CKT 1  /* BADIN    100 - 3BADIN 2 115 */
/* END
CONTINGENCY BADIN1001152
TRIP BRANCH FROM BUS 339001 TO BUS 304343 CKT 1 /* BADIN    100 - BADIN #2 115 */
END
/* CONTINGENCY PISGH1001151
/* OPEN BRANCH FROM BUS    306190 TO BUS  40750 CKT 1  /* PISGAH   100 - 3PISGAH  115 */
/* END
CONTINGENCY PISGH1001151
OPEN BRANCH FROM BUS 306190 TO BUS 304750 CKT 1 /* PISGAH   100 - PISGAH   115 */
END
/* CONTINGENCY PISGH1001152
/* OPEN BRANCH FROM BUS    306190 TO BUS  40750 CKT 2  /* PISGAH   100 - 3PISGAH  115 */
/* END
CONTINGENCY PISGH1001152
OPEN BRANCH FROM BUS 306190 TO BUS 304750 CKT 2 /* PISGAH   100 - PISGAH   115 */
END
/******************************   BULK END   ************************************/
/******************************   ABNORMAL long BEGINS   ************************************/
CONTINGENCY AB_BUSHRBK1    /* 031411 works before VCSummer
TRIP BRANCH FROM BUS 306233 TO BUS 370102 CKT 1 /* BUSH RIVER BL 230 KV LINE
TRIP Bus 309404 /* bush river bk 306001
END
CONTINGENCY AB_BUSHRBK1  /*  031411 works after VCSummer
TRIP BRANCH FROM BUS 306233 TO BUS 370211 CKT 1 /* BUSH RIVER BL 230 KV LINE
TRIP Bus 309404 /* bush river bk 306001
END
CONTINGENCY AB_HODGBK1_L
TRIP BRANCH FROM BUS 306005 TO BUS 306003 CKT 1 /* CHICKASAW 230 KV LINE
TRIP Bus 309418 /* HODGES 230-100 KV BK 306001
/* OPEN ALREADY TRIP BRANCH FROM BUS 307088 TO BUS 309418 CKT 1
END
CONTINGENCY AB_HODGBK2_L
TRIP BRANCH FROM BUS 306005 TO BUS 306003 CKT 1 /* CHICKASAW 230 KV LINE
TRIP Bus 309419 /* HODGES 230-100 KV BK 2
END
CONTINGENCY AB_LAKEBK2_L /* updated 06112012
OPEN BRANCH FROM BUS 308350 TO BUS 306543 CKT 1 /* PINOCA bl 230 KV LINE
OPEN bus 309420 /* LAKEWOOD 230/100 KV BK 2
/* OPEN BRANCH FROM BUS 308166 TO BUS 309420 CKT 2 /* TERT OPEN 3/99 RDG
/* OPEN BRANCH FROM BUS 308166 TO BUS 308158 CKT 1 /* SPURRIER LINE ADDED 3/99 RDG
END
CONTINGENCY AB_LAKEBK3_L /* updated 06112012
OPEN BRANCH FROM BUS 306539 TO BUS 308543 CKT 2 /* PINOCA wh 230 KV LINE
OPEN BUS 309421 /* LAKEWOOD 230/100 KV BK 306003
/*OPEN BRANCH FROM BUS 308166 TO BUS 308158 CKT 1 /* SPURRIER LINE r/m 2/20/2006 cam
END
/* CONTINGENCY AB_MCDOBK1_L  /* REMOVED 081310
/* OPEN BRANCH FROM BUS 306442 TO BUS 306444 CKT 1 /* MCDOWELL 230 KV LINE
/* OPEN BRANCH FROM BUS 306444 TO BUS 309426 CKT 1 /* MCDOWELL 230-100 KV BK 1
/* OPEN BRANCH FROM BUS 306473 TO BUS 309426 CKT 1 /* MCDOWELL 230-100 KV BK 1
/* OPEN BRANCH FROM BUS 307998 TO BUS 309426 CKT 1 /* MCDOWELL 230-100 KV BK 1
/* END
CONTINGENCY AB_MCDOBK2_L
OPEN BRANCH FROM BUS 306442 TO BUS 306444 CKT 1 /* MCDOWELL 230 KV LINE
OPEN BUS 309427 /* MCDOWELL 230-100 KV BK 2
END
CONTINGENCY AB_MORNBK3_L
TRIP BUS 309551/* MORNING STAR 230-100 KV BK 306003
OPEN BRANCH FROM BUS 306541 TO BUS 306542 CKT 1 /* GOOSE CK 230 KV LINE
END
CONTINGENCY AB_MORNBK4_L
TRIP BUS 309552 /* MORNING STAR 230-100 KV BK 306004
OPEN BRANCH FROM BUS 306541 TO BUS 306333 CKT 1 /* SANDY RIDGE 230 KV LINE
END
CONTINGENCY AB_PEACBK1_L /* updated 05182012
OPEN BRANCH FROM BUS 306334 TO BUS 306332 CKT 1 /* PEACOCK wh 230 KV LINE
TRIP BUS 309448 /* PEACOCK 230-100 BK 1
END
CONTINGENCY AB_PEACBK2_L
OPEN BRANCH FROM BUS 308334 TO BUS 306332 CKT 2 /* PEACOCK bl 230 KV LINE
TRIP BUS 309449 /* PEACOCK 230-100 BK 2
END
CONTINGENCY AB_SHADBK1_L
TRIP BUS 309459 /* SHADY GROVE 230-100 KV BK 306001
TRIP BRANCH FROM BUS 306109 TO BUS 306104 CKT 1 /* 230 KV TAP LINE
END
CONTINGENCY AB_SHADBK2_L
TRIP BUS 309460 /* SHADY GROVE 230-100 KV BK 2
TRIP BRANCH FROM BUS 306109 TO BUS 306105 CKT 2 /* 230 KV TAP LINE
END
CONTINGENCY AB_TUCKBK2_L
OPEN BRANCH FROM BUS 308489 TO BUS 306106 CKT 1 /* 6TUCKASE 230 - 6JOCASSE 230 */
OPEN BRANCH FROM BUS 308489 TO BUS 308487 CKT 2 /* TUCKASEGEE 230/161 BANK 2
END
CONTINGENCY AB_TUCKBK3_L
OPEN BRANCH FROM BUS 308489 TO BUS 306106 CKT 1 /* 6TUCKASE 230 - 6JOCASSE 230 */ jcc added 09302007
OPEN BRANCH FROM BUS 308489 TO BUS 308487 CKT 3 /* TUCKASEGEE 230/161 BANK 3
END
CONTINGENCY AB_WOODBK4_L
OPEN BRANCH FROM BUS 306545 TO BUS 306331 CKT 1 /* STEELBERRY 230 KV LINE
TRIP BUS 309471 /* WOODLAWN 230-100 KV BK 306004
END
CONTINGENCY AB_WOODBK5_L
OPEN BRANCH FROM BUS 306545 TO BUS 306331 CKT 1 /* STEELBERRY 230 KV LINE
TRIP BUS 309472 /* WOODLAWN 230-100 KV BK 306005
END
/******************************   ABNORMAL END   ************************************/
/****************   EXTERNAL TO DUKE CONTROL AREA BEGIN   ***********************/
/******************   EXTERNAL TO DUKE CONTROL AREA END   ***********************/
/**********************   OTHER CONTINGENCIES BEGIN   ***************************/

CONTINGENCY NCPWG2
TRIP BRANCH FROM BUS 304332 TO BUS 304331 CKT 1 /* ASHEB    230 - ASHEB    115 */
END
END
/* CONTINGENCIES RAN