| O.O. | 16-00317-OO | MISO No. | 1-11788910 | File No. | 240803 |
| --- | --- | --- | --- | --- | --- |
| Name of Outage: | Dorsey 500 kV Bank T51 |
| Effective Dates: | 2016-11-26 0500 to 2016-11-26 2000 CDT (2016-11-26 0600 to 2016-11-26 2100 EST) |
| Standing Guide Reference: | MHEX – USA Winter Standing Guide |

| Description of Work: | Commission Dorsey 230 kV Breaker R36. |
| --- | --- |
| TRANSFER LIMITS: |
| MH-USA South (MH Export) |
|  |  |  | SOL: | 2175 |  | Schedule Limit | 1950 |
| Location |  | RM |  | CRSG | OM |  |  | Schedule Limit |
|  | TTC |  | Transfer (SOL) |  |  | Firm | Non-Firm |  |
| USA | 2470 | 295 | 2175 | 150 | 75 | 1950 | 0 | 1950 |
| MH-USA North (MH Import) |
| IROL | 1000 |  | SOL: | 900 |  | Schedule Limit | 850 |
| Location |  | RM |  | CRSG | OM |  |  | Schedule Limit |
|  | TTC |  | Transfer (SOL) |  |  | Firm | Non-Firm |  |
| USA | 945 | 45 | 900 | 0 | 550 | 350 | 500 | 850 |
| TLR Triggers | South TLR 1 | South TLR 3 | North TLR 1 | North TLR 3 |  |
|  | 2005 | 2025 | 837 | 855 |  |
| MISO Webtool Postings | MISO Webtool Postings TTC TRM Coeff MHEX_S (Export) 2470 520 1.000 MHEX_N (Import) 945 595 0.160 |

| MHEB Internal Transfer Limits | D603M (Remaining 500 kV Bank) South TLR Triggers D603M_S TLR 1 D603M_S TLR 3 1105 1129 TTC Transfer (SOL) OM Control Point 1188 1188 50 1138 |
| --- | --- |

| Special Notes to MISO North RC | A) During this prior outage condition generation curtailment of the St. Joseph and St. Leon wind farms concurrent with TLR on MHEX_N may be required when Manitoba to USA flows are north to prevent post contingent overloads on G37C following a trip of B10T or M602F. B) The SOL for MHEX_S and MHEX_ N are the same if the MISO RTCA and MISO Flowgate Monitoring Tool is unavailable prior to or during this outage. |
| --- | --- |

| Special Instructions to MHEB Operator: | A) TOI Extentions - This TOI may be extended until 23:59 by performing the following steps: Verify system conditions to confirm there are no additional tie line facilities outages, or new internal MH outages. Review RTCA to confirm there are no new contingencies. Contact MISO to confirm there are no new outages, if there are no new outages provide notice to MISO that MH is extending the TOI. Extend the outage in COLA. Update TLAP outage table. Provide notice to affected balancing authorities |
| --- | --- |

| Special Instructions to MHEB Operator (cont): | B) When called upon by MISO for the supply of CRSG: If Real Time Contingency Analysis (RTCA) indicates a post contingent overload condition on Y51L for the contingent loss of D14S - redispatch MH generation to maintain CRSG delivery as per: Start Brandon Gas Generation and run up to 60 MW. Brandon generation must be re-dispatched from HVDC generation at Dorsey After 60 MW re-dispatch is complete, should RTCA continues to indicate a post contingent overload condition on Y51L due to the contingent loss of D14S, Continue to re-dispatch generation from Brandon gas in 10 MW increments until post contingent overload on Y51L has been mitigated. The mitigation must be completed within 30 minutes. C) Set Bank 52 MW Limits on Dorsey 500 One-line as per D603M Limits Set ‘NORM’ alarm to Control Point and ‘MAX’ alarm to SOL Re-dispatch generation or reduce exports as required to reduce flow below control point |
| --- | --- |
| Prepared By: | Hogeveen Rutter | Date: | 2016 11 15 |

Copies to:

SOSS, System Control Centre			MISO

NSSS, System Control Centre			GSO, System Control Centre

GSSS, System Control Centre