Updated Path C Posting

Posted for Customer Comment

3/22/2011

Background:

The recent addition of the double circuit 345 kV line from Populus to Terminal yielded a higher path rating for Path C.  The previous total transfer capability (TTC) of 980 MW is now 1600 MW.  This higher rating has been posted for the Path C element, however enhancements to OASIS scheduling topology is required to maximize the flexibility of the transmission system.

In order to take advantage of the additional segments from the north, southbound across Path C, it is necessary to post a more granular topology as there are several lines and alternative routes on the north side of Path C each with significant ratings.  See attached diagram.

This more granular topology requires that specific routes across the path be posted.  The challenge is that OASIS only allows one path with the same POR and POD combination.  For instance we cannot manage a path of JBSN to PACE with one route being JBSN to Populus to PACE and one being JBSN to Wyoming to PACE.

Proposed Solution:

To use the maximum flexibility and capability of the transmission system, new segments will be posted and customers can use the different segments, combining the segments using linked AREFs, to define and utilize a specific route.  It was determined that this solution, while complicated, is the most user friendly and can be implemented on PacifiCorp’s current OASIS.

Details:

See attached page with diagram showing points of receipt and delivery as well as transmission segments for the Path C portion of PacifiCorp’s transmission system.

Please provide comments to this proposal at transmission.service@pacificorp.com by April 22, 2011.

Example for additional Path C topology

Current route (with path segments) will not change and is show below:

- Route: JBSN-PACE

- Segments: JBSN-WYOC, WYOC-TRONA, TRONA-NUT, NUT-PACE

For current reservations there will be no change and the above paths will remain the main route to get from JBSN to PACE.  As seen in the below diagram there are additional routes that will be available with the addition of Populus (POP).

Potential additional routes will include but may not be limited to the below list:

- JBSN-POP

- POP-JBSN

- POP-PACE segments include POP-PATHC, PATHC-NUT, NUT-PACE

- POP-JBWT

- JBWT-POP

- BORA-JBWT

- JBWT-BORA

For example point to point customers that have a current reservation on the main route highlighted in green will need to redirect that reservation to one of the adjacent routes and link the redirect to any subsequent adjacent routes until the final POD has been reached and as long as all reservations are used on the same tag there will be only one charge.

Network customers that have a current reservation on the main route highlighted in green will be allocated appropriate transmission on each on the new routes as identified in the network allocation study.

All of the above POR/POD combinations are interconnection boundaries with the PACE Balancing Area or are in the PACE Balancing Area with the exception of JBWT which is in the PACW Balancing Area and POP which is in both Balancing Areas.