| Business Units: | All Business Units |
| --- | --- |
| Date Range: | all dates on or before 04/11/2018 |
| Equipment Classes: | Bus, Capacitor, Circuit Breaker, Circuit Switcher, Disconnect Switch, Switchgear, Transformer, Transmission Circuit |
| Generate By: | Control Center: PSE Transmission Control Center |

| OUTAGE REQUESTS |
| --- |
| Outage #/ Revision/ Status | Station/ Circuit/Equipment | Requested Date Range/ Duration | From/To/Type | Required Approvals | Path(s) Affected | Requested By/ Reason/Priority |
|  |  |  |  |  | Path | OTC Impact | WECC OTC Seas. Ratings |  |
| 1-00521773 Revision #1 Implemented Verified | Berrydale 115kV 142_M, Berrydale 115kV SW142_CAP, Berrydale Capacitor Bank OOS | 2017/10/18 to 2018/02/28 133.25 Days | 11:00 - 16:00 Continuous |  |  |  |  | Baker, Wesley Berrydale Capacitor Bank unavailable during switch repair and panel upgrade. Isolation point is Berrydale 142 main bus disconnect. |
| 1-00518509 Revision #7 Implemented Verified | Talbot Hill 230kV 7627, Talbot Hill 230kV 7629, Talbot Hill 230kV 7630, Talbot Hill 230kV 7631, Talbot Hill 230kV 7633 OOS | 2017/10/30 to 2018/07/30 273.17 Days | 12:00 - 16:00 Continuous |  |  |  |  | Parker, David Talbot Hill 230kV East Bus project |
| 1-00536169 Revision #6 Implemented Unverified | Portal Way P800 BP&C over AUX bus PCB 799 OOS | 2017/12/19 to 2018/01/17 29.33 Days | 08:00 - 16:00 Continuous |  |  |  |  | Poliquin, David Breaker Replacement |
| 1-00537517 Revision #6 Implemented Unverified | Berrydale 115kV 499 BP&C OOS | 2018/01/02 to 2018/01/11 9.33 Days | 08:00 - 16:00 Continuous |  |  |  |  | Parker, David Breaker replacement |
| 1-00532702 Revision #8 Implemented Unverified | Olympia - Saint Clair #2 115 kV Line : Olympia - McKinley OOS | 2018/01/03 to 2018/01/26 23.35 Days | 07:30 - 16:00 Return Evenings and Weekends |  |  |  |  | Parker, David Relocating poles |
| 1-00535118 Revision #6 Implemented Unverified | Sammamish - Moorlands #1 115 kV Line : Inglewood - Juanita OOS | 2018/01/08 to 2018/01/16 8.44 Days | 07:30 - 18:00 Return Evenings and Weekends |  |  |  |  | Parker, David Cell site |
| 1-00535930 Revision #7 Implemented Unverified | Christopher - Starwood 115 kV Line : Marine View - Weyerhauser Tap OOS | 2018/01/08 to 2018/01/11 3.42 Days | 07:30 - 17:30 Return Evenings |  |  |  |  | Parker, David Replacing poles |
| 1-00535615 Revision #11 Implemented Unverified | Valley Junction - Foss Corner 115 kV Line : Poulsbo Tap - Foss Corner OOS | 2018/01/08 to 2018/01/12 3.44 Days | 19:30 - 06:00 Continuous |  |  |  |  | Parker, David Relocating 2 poles |
| 1-00539136 Revision #3 Implemented Unverified | Sedro Woolley - Bellingham #4 115 kV Line : Norlum - Alger OOS | 2018/01/09 to 2018/01/13 4.48 Days | 06:30 - 18:00 Continuous |  |  |  |  | Parker, David Transmission rebuild |
| 1-00540235 Revision #3 Implemented Unverified | Summit - Skykomish 115 kV Line : Skykomish - Scenic Tap - CHPD Summit OOS | 2018/01/10 to 2018/01/11 28 Hours | 15:00 - 19:00 Continuous |  |  |  |  | Shore, Daniel Unknown fault location. Helicopter patrol scheduled for 1/11 AM. |
| 1-00535289 Revision #6 RC OPA D+1 Confirmed | White River - Alderton #4 115 kV Line : Stewart Tap - Alderton BP&C OOS | 2018/01/11 to 2018/01/11 3.5 Hours | 06:30 - 10:00 Continuous |  |  |  |  | Parker, David Alderton West 115kV Bus for commissioning 230kV |
| 1-00535298 Revision #6 RC OPA D+1 Confirmed | Fairchild - Alderton 115 kV Line : Shaw - Alderton, White River - Alderton #4 115 kV Line : Stewart Tap - Alderton OOS | 2018/01/11 to 2018/01/11 3 Hours | 10:00 - 13:00 Continuous |  |  |  |  | Parker, David Alderton West and Mid 115kV bus for 230kV commissioning |
| 1-00539731 Revision #1 TOP Confirmed | Berrydale 115kV 498 BP&C OOS | 2018/01/12 to 2018/01/26 14.33 Days | 08:00 - 16:00 Continuous |  |  |  |  | Kauer, Kaysee Breaker replacement |
| 1-00538477 Revision #4 RC Short-Range Confirmed | Christopher - Starwood 115 kV Line : Marine View - Weyerhauser Tap OOS | 2018/01/15 to 2018/01/16 1.44 Days | 06:30 - 17:00 Return Evenings |  |  |  |  | Parker, David |
| 1-00537256 Revision #3 RC Short-Range Confirmed | Bangor - Foss Corner 115 kV Line : Bangor - Foss Corner OOS | 2018/01/16 to 2018/01/17 1.46 Days | 06:00 - 17:00 Continuous |  |  |  |  | Parker, David Replacing pole |
| 1-00540110 Revision #1 TOP Confirmed | Wind Ridge - Kittitas 115 kV Line : Wind Ridge - Kittitas OOS | 2018/01/16 to 2018/01/16 9 Hours | 07:00 - 16:00 Continuous |  |  |  |  | Parker, David Replacing broken cross arm |
| 1-00535699 Revision #3 RC Short-Range Confirmed | Talbot Hill - Berrydale #1 115 kV Line : Panther Lake Tap - Glencarin OOS | 2018/01/17 to 2018/01/19 2.44 Days | 07:30 - 18:00 Return Evenings |  |  |  |  | Parker, David Cell site |
| 1-00535936 Revision #3 RC Short-Range Confirmed | Christopher - Starwood 115 kV Line : Marine View - Weyerhauser Tap OOS | 2018/01/17 to 2018/01/17 10 Hours | 07:30 - 17:30 Continuous |  |  |  |  | Parker, David Relocate pole |
| 1-00539711 Revision #2 RC Short-Range Confirmed | Olympia - Saint Clair #2 115 kV Line : McKinley - N.O. Sw 167 - Johnson Hill Tap, Olympia - Saint Clair #2 115 kV Line : Pleasant Glade Tap - Lacey, Olympia - Saint Clair #2 115 kV Line : Johnson Hill Tap - Pleasant Glade OOS | 2018/01/17 to 2018/01/18 9 Hours | 21:00 - 06:00 Continuous |  |  |  |  | Kauer, Kaysee removing mobile sub and energizing new bank at Johnson Hill substation |
| 1-00540108 Revision #2 RC Short-Range Confirmed | BPA Kitsap - Valley Junction 115 kV Line : Chico Tap - Silverdale Tap OOS | 2018/01/18 to 2018/01/26 8.33 Days | 08:00 - 16:00 Return Evenings and Weekends |  |  |  |  | Parker, David Proximity work |
| 1-00537358 Revision #2 TOP Confirmed | White River - Krain Corner #1 55 kV Line : Krain Corner - Wabash OOS | 2018/01/19 to 2018/01/19 10.5 Hours | 06:30 - 17:00 Continuous |  |  |  |  | Parker, David Replace bolt |
| 1-00535919 Revision #7 TOP Proposed | Portal Way - Arco Central 115 kV Line : Portal Way - Arco Central OOS | 2018/01/22 to 2018/01/26 4.42 Days | 07:00 - 17:00 Continuous |  |  |  |  | Parker, David Relocate transmission poles |
| 1-00537817 Revision #3 TOP Proposed | Sedro Woolley - Bellingham #4 115 kV Line : Norlum - Alger OOS | 2018/01/22 to 2018/02/05 14.42 Days | 08:00 - 18:00 Continuous |  |  |  |  | Parker, David Transmission rebuild |
| 1-00539753 Revision #1 TOP Proposed | BPA Kitsap - South Bremerton #1 115 kV Line : BPA Kitsap - South Bremerton OOS | 2018/01/23 to 2018/01/23 9.5 Hours | 06:30 - 16:00 Continuous |  |  |  |  | Kauer, Kaysee end to end testing |
| 1-00538270 Revision #1 TOP Proposed | White River - Fairchild 115 kV Line : Sumner - Woodland OOS | 2018/01/30 to 2018/01/31 1.42 Days | 08:00 - 18:00 Continuous |  |  |  |  | Parker, David Replacing corner pole |
| 1-00531629 Revision #2 TOP Confirmed | SCL Cedar Falls - Lake Youngs 115kV Line Cedar Falls - Lake Youngs 115kV line OOS | 2018/02/01 to 2018/02/02 1.67 Days | 06:00 - 22:00 Continuous |  | Path 3 | /a | 3150 MW N->S 2000 MW S->N | Hickey, John Pole Replacement @ 11/147 and 11/082 on the Cedar Falls - Lake Youngs 115kV line |
| 1-00532783 Revision #1 TOP Proposed | BPA Monroe - Novelty Hill 230 kV Line : BPA Monroe - Novelty Hill OAT, Sammamish - Novelty Hill #2 230 kV Line : Novelty Hill - Sammamish OAT, Novelty Hill 230/115kv Bank OAT OOS | 2018/02/01 to 2018/02/01 30 Mins | 10:00 - 10:30 Noncontinuous |  | Path 3 | /a | 3150 MW N->S 2000 MW S->N | Parker, David Breaker profiling, one at a time |
| 1-00540225 Revision #2 TOP Proposed | Everett BRK 3574 OOS | 2018/02/07 to 2018/02/07 8.5 Hours | 07:00 - 15:30 Continuous |  | Path 3 | /a | 3150 MW N->S 2000 MW S->N | Dotson, Jim TESTING ON 115KV BRK 3574. OPENS EVERETT 115KV RING BUS |
| 1-00540119 Revision #2 TOP Proposed | SCL Bothell - Sammamish 230kV Line Bothell Substation to Sammamish Substation 230kv line, SCL Diablo - SCL Bothell #1 230kV Line Diablo Substation to Shoreline Substation #1 230kV Line, SCL Bothell 230kV Bus 2 Bothell Substation 230kV Bus 2, SCL Bothell Bank #62 Bothell Substation Bank 62, SCL Bothell BKR 120-BK62 Bothell Substation Breaker 120 Bank 62, SCL Bothell BKR 240-66 Bothell Substation Breaker 240-66, SCL Bothell BKR 240-67 Bothell Substation Breaker 240-67, SCL Bothell BKR 240-68 Bothell Substation Breaker 240-68, SCL Bothell BKR 240-69 Bothell Substation Breaker 240-69, SCL Bothell LI 240-BK62 Bothell Substation Load Interrupter 240 Bank 62 OOS | 2018/03/26 to 2018/03/31 5.71 Days | 05:00 - 22:00 Continuous |  | Path 3 | /a | 3150 MW N->S 2000 MW S->N | Sandoval, Marcus Breaker 240-69 Relay Upgrade. Disconnect Upgrades. |
| 1-00539164 Revision #1 TOP Proposed | BPA Maple Valley - Talbot Hill #1 230 kV Line : BPA Maple Valley - Talbot Hill, Talbot Hill - Berrydale #3 230 kV Line : Talbot Hill - Berrydale, Talbot Hill 230/115kv Bank 1 OOS | 2018/04/02 to 2018/09/28 179.33 Days | 08:00 - 16:00 Continuous |  | Path 3 | /a | 3150 MW N->S 2000 MW S->N | Parker, David Talbot Hill 230kV South Bus rebuild |