Transmission Outage Information

Posted:  06/16/08 11:15

Dennis Murray – Transmission Services

See SPP Oasis for the latest restoration estimates

To access use ctrl + left mouse click on link below

Transmission Outage Restore Information

Outages:

- Jeffrey to Summit 345 KV:

06/12/08 09:00-Description: Thus far located 13 Structures down just east of Salina.

Start Time: 06/12/2008 06:00

Return to service:	6/16 0221

- Summit to Northview 115 kV:

06/12/08 09:00-Description: Two structures are down.

Start Time: 06/12/2008 06:00

Return to service:	6/15 2025

- Northview to Abilene Energy Center 115 kV:

06/12/08 09:00-Description: A structure on the JEC to Summit 345 kV line went down at the point where the line crosses the Northview to Abilene Energy Center 115 kV line.  The 345 kV conductor is laying down over the 115 kV line.  The 345 kV structure will be replaced first to remove the conductors from the 115 kV line.

Start Time: 06/12/2008 06:00

Returned to service  06/13/08 1439

- Wildcat Creek to Stagg Hill 115 kV:

06/12/08 09:00-Description:  One structure down.  The conductor has been tied off to allow emergency vehicle access into the local area in Manhattan.  Restoring this line is a low priority.

Start Time: 06/12/2008 06:00

Return to service:

- King Hill to Circleville 115 KV:

06/12/08 06/12/08 09:00-Description:  Assessing damage

Start Time: 06/12/2008 06:00

Return to service:

- Tecumseh Hill to Kelly 161 KV:

06/12/08 09:00-Description:  Assessing damage

Start Time: 06/12/2008 06:00

Return to service:

General:  When the weather permits, an aerial patrol will be performed.