Scheduling across MP-ONT interface beginning September 1, 2007

New Reservations

Source/Sink - Due to the introduction of the new ONT_W node interface into the MISO Commercial Model, for transactions active September 1, 2007 and beyond, transmission service moving across the MP-ONT interface on the MISO page of the MISO OASIS node must utilize a source/sink of ONT_W.

POR/POD – MP-ONT should continue to be designated as a POR/POD as appropriate.

Existing Reservations

Existing reservations (submitted before ONT_W is made reservable) active as of September 1, 2007 on the MISO page of the MISO OASIS node that reference the MP-ONT interface will not be modified, but will be required to be tagged according to below instructions.

Scheduling of Transactions

Transactions with a MISO reservation source or sink of ONT_W must be scheduled with source or sink of ONT_W.

Existing Transactions with a MISO reservation source or sink of ONT across the MP-ONT interface must be scheduled with source or sink of ONT_W.

MP-ONT will be selected as the POR or POD on the MISO TSR and should be scheduled in the same manner.

Note: The ONT_W source/sink points must be registered in TSIN by each Market Participant in order for it to be selectable in the eTag dropdown.

Example:

# MISO Transmission-Existing Reservation

Source		POR		POD		SINK

ONT		MP-ONT	MP		MP

# MISO Transmission-New Reservation

Source		POR		POD		SINK

ONT_W	MP-ONT	MP		MP

# All-Tags Transaction Path – Active dates 9/1/2007 and beyond

| Source | ONT_W |  |  |
| --- | --- | --- | --- |
| CA | TP | POR | POD | S/E |
| ONT |  |  |  |  |
|  | ONT | ONT | ONT.EXPORT.INTFALLS.PS | ONT |
|  | MISO | MP-ONT | MP | MISO |
| MISO |  |  |  |  |
| Sink | MP.xxxx |  |  |  |

Scheduling of Spot Transactions

Transactions sourcing at ONT_W, flowing across the MP-ONT interface and sinking into the MISO footprint may not use a Spot Market TSR. MISO Import transactions across this interface must be represented with an incremental TSR designating an internal MISO-BA CPNode as the sink.

Previously Scheduled Transactions

Transactions currently existing on the MP-ONT interface for active dates September 1, 2007 and beyond will have to be terminated and replaced with an e-Tag reflecting the new ONT_W source/sink.

ONT_W transactions will be available to reserve on the MISO OASIS on: August 24, 2007 for transactions active after September 2007

ONT_W transactions will be available to tag on: August 24, 2007 for transactions active after September 2007 – assuming that the source/sink point of “ONT_W” has been properly registered in TSIN and updated in eTag software.